## Slide 1
Larana Electric Car
CHARGING TECHNIQUES OF
EV BATTERY
Fast
Modern
Efficient

## Slide 2
  Battery charging significantly affects the performance, efficiency, and lifespan of rechargeable batteries used in applications like electric vehicles and portable devices.
  Various charging techniques such as CC, CV, CC–CV, and temperature-based methods are used to balance charging speed and safety.
  Each method has distinct characteristics in terms of voltage and current behavior, along with specific advantages and limitations.
INTRODUCTION
PROBLEM STATEMENT
To design and simulate a battery charging system using different charging methods to achieve fast ,efficient, and safe , charging of lithium ion battery

## Slide 3
MOTIVATION
  The increasing use of rechargeable batteries in EVs and electronics requires efficient and safe charging methods.
Different charging techniques affect temperature, speed, safety, and battery life in different ways.
Understanding these effects is important to improve battery performance and reliability.

## Slide 4
OBJECTIVES
Larana Electric Car
Safety
Temperature
Battery Life
Speed
To evaluate the safety of each charging method in terms of overcharging, overheating, and risk of battery damage
To analyze how different charging techniques affect battery temperature and thermal behavior during charging.
To study the impact of charging methods on battery health and overall cycle life.
To compare the charging speed of different techniques by measuring the time taken to reach full charge

## Slide 5
CC METHOD
Constant Current (CC) charging means supplying a steady current to the battery so it charges quickly, especially when it’s low on charge. As the battery fills up, its voltage rises.
  We observed that In constant current charging, the battery charges very rapidly without proper voltage control.
  This is causing the battery voltage to exceed its safe limit during charging.
  It leads to overcharging, overheating, and reduceing battery life.

## Slide 6
CC METHOD

## Slide 7
CV METHOD
Constant Voltage (CV) charging maintains a fixed voltage across the battery during charging. As the battery charges, the current gradually decreases while the voltage remains constant.
  We observe that, In constant voltage charging, the voltage is maintained fixed, causing the charging current to gradually decrease.
  This results in a very slow charging process, so it takes long time to reach 100% state of charge (SOC).

## Slide 8
CV METHOD

## Slide 9
CC-CV METHOD
CC–CV charging is a two-stage method that combines constant current and constant voltage charging. In the first stage, the battery is charged with a constant current, causing the voltage to gradually increase. Once the battery reaches its set maximum voltage, the method switches to constant voltage mode. In this second stage, the voltage is kept constant while the current slowly decreases. This approach ensures efficient charging in the beginning and safer, controlled charging as the battery reaches full capacity.
In this method we are able to control the overcharging and can reduce the charging time
But the charging control is more complex, requiring precise switching between constant current and constant voltage modes.

## Slide 10
CC-CV METHOD

## Slide 11
CC-CV METHOD

## Slide 12
CT-CV METHOD
CT–CV charging combines temperature-based control with constant voltage charging. In the initial stage, the charging current is adjusted based on the battery’s temperature to prevent overheating. As the battery approaches its safe voltage limit, the method switches to constant voltage mode. In this stage, the voltage is held constant while the current gradually decreases
  In CT–CV charging, a thermal model is developed to monitor battery behavior during charging. This model helps in observing both internal temperature and surface temperature in real time.

## Slide 13
CT-CV METHOD

## Slide 14
CURRENT Vs TIME
Vbattery Vs TIME

## Slide 15
SURFACE TEMP Vs TIME
THERMAL MODEL USING REAL COMPONENTS

## Slide 16
  CC
  CV
  CC-CV
  CT-CV
61 min
104 min
91 min
80 min
  ΔT=6.5°C
  ΔT=6.5°C
RESULTS
METHOD
CHARGING TIME
TEMPERATURE RISE

## Slide 17
CONCLUSION
  The proposed charging profile reduces the overall charging time compared to the conventional CC–CV method.
  It effectively limits the temperature rise by incorporating thermal control during charging.
  Thus, the CT-CV method ensures faster, safer, and more efficient battery charging performance.
REFERENCE:
IEEE PAPERS:
A Closed-Loop Constant-Temperature Constant-Voltage Charging Technique to Reduce Charge Time of Lithium-Ion Batteries
Performance Analysis of the Lithium-Ion Batteries using CT-CV Charging Technique

## Slide 18
Larana Electric Car
Thank You!
Fast
Modern
Efficient
project by
ANKIT VERMA-240002008
MIDATANA DHILEEP-240002038
PANKAJ KUMAR-240002048
SIDDHARTHA PORIKA-240002071
SATHVIK RATHOD-240002067